## Slide 1: Parallel & Distributed Computing Lecture 3: General Parallelism Terms
Department of Computer Science
NUML, Islamabad
Farhad M. Riaz
Farhad.Muhammad@numl.edu.pk

## Slide 2: von Neumann Architecture
Authored the general requirements for an electronic computer in his 1945 papers
Also known as "stored-program computer”
Both program instructions and data are kept in electronic memory
Since then, virtually all computers have followed his design
John von Neumann

## Slide 3: Von Neumann Architecture Four main Components
Read/write, random access memory is used to store both program instructions and data
  Program instructions are coded data which tell the computer to do something
  Data is simply information to be used by the program
Control unit fetches instructions/data from memory, decodes the instructions and then sequentially coordinates operations to accomplish the programmed task.
Arithmetic Unit performs basic arithmetic operations
Input/Output is the interface to the human operator
parallel computers still follow this basic design
Just multiplied in units

## Slide 4: Flynn's Classical Taxonomy
Different ways to classify parallel computers
One of the more widely used classifications, in use since 1966, is called Flynn's Taxonomy
Distinguishes multi-processor computer architectures according to two dimensions
  Instruction Stream
  Data Stream

## Slide 5: SISD (Scalar Processing)
A serial (non-parallel) computer
Single Instruction: Only one instruction stream is being acted on by the CPU during any one clock cycle
Single Data: Only one data stream is being used as input during any one clock cycle
Deterministic execution
This is the oldest type of computer
Examples: older generation mainframes, minicomputers, workstations and single processor/core PCs.

## Slide 6: SIMD (Vector Processing)
Single Instruction: All processing units execute the same instruction at any given clock cycle
Multiple Data: Each processing unit can operate on a different data element
Best suited for specialized problems such as graphics/image processing.
Synchronous and deterministic execution
Processor Arrays Vector Pipelines
Examples:
  Processor Arrays: Thinking Machines CM-2
  Vector Pipelines: IBM 9000
  Most modern computers with GPU units

## Slide 7: Scalar vs Vector (SIMD)

## Slide 8: Multiple Instruction, Single Data (MISD)
Multiple Instruction: Each processing unit operates on the data independently via separate instruction streams.
Single Data: A single data stream is fed into multiple processing units.
Few (if any) actual examples of this class of parallel computer have ever existed.
Some conceivable uses might be:
  multiple frequency filters operating on a single signal stream
  multiple cryptography algorithms attempting to crack a single coded message.

## Slide 9: Multiple Instruction, Multiple Data (MIMD)
Multiple Instruction: Every processor may be executing a different instruction stream
Multiple Data: Every processor may be working with a different data stream
Execution can be synchronous or asynchronous, deterministic or non-deterministic
Currently, the most common type of parallel computer - most modern supercomputers fall into this category
Examples: most current supercomputers, networked parallel computer clusters, grids, multi-core PCs

## Slide 10: MIMD Classification
Shared Memory
Distributed Memory

## Slide 11: Shared vs Distributed Memory

## Slide 12: Some General Parallel Terminology
Supercomputing / High Performance Computing (HPC)
  Using the world's fastest and largest computers to solve large problems
Node
  A standalone "computer in a box". Usually comprised of multiple CPUs/processors/cores, memory, network interfaces, etc. Nodes are networked together to comprise a supercomputer.
CPU / Socket / Processor / Core
  In the past, a CPU (Central Processing Unit) was a singular execution component
  Then, multiple CPUs were incorporated into a node
  Then, individual CPUs were subdivided into multiple "cores", each being a unique execution unit
  CPUs with multiple cores are sometimes called "sockets”
  The result is a node with multiple CPUs, each containing multiple cores

## Slide 14: Some General Parallel Terminology
Task
  A logically discrete section of computational work. A task is typically a program or program-like set of instructions that is executed by a processor. A parallel program consists of multiple tasks running on multiple processors.
Pipelining
  Breaking a task into steps performed by different processor units, with inputs streaming through, much like an assembly line; a type of parallel computing.
Shared Memory
  From a strictly hardware point of view, describes a computer architecture where all processors have direct (usually bus based) access to common physical memory. In a programming sense, it describes a model where parallel tasks all have the same "picture" of memory and can directly address and access the same logical memory locations regardless of where the physical memory actually exists.

## Slide 15: Some General Parallel Terminology
Symmetric Multi-Processor (SMP)
  Shared memory hardware architecture where multiple processors share a single address space and have equal access to all resources.
Distributed Memory
  In hardware, refers to network based memory access for physical memory that is not common. As a programming model, tasks can only logically "see" local machine memory and must use communications to access memory on other machines where other tasks are executing.
Communications
  Parallel tasks typically need to exchange data. There are several ways this can be accomplished, such as through a shared memory bus or over a network, however the actual event of data exchange is commonly referred to as communications regardless of the method employed

## Slide 16: Some General Parallel Terminology
Synchronization
  The coordination of parallel tasks in real time, very often associated with communications.
  Often implemented by establishing a synchronization point within an application where a task may not proceed further until another task(s) reaches the same or logically equivalent point.
  Synchronization usually involves waiting by at least one task and can therefore cause a parallel application's wall clock execution time to increase.
Granularity
  granularity is a qualitative measure of the ratio of computation to communication
  Coarse: relatively large amounts of computational work are done between communication events
  Fine: relatively small amounts of computational work are done between communication events
Observed Speedup
  Observed speedup of a code which has been parallelized, defined as:
wall-clock time of serial execution
-----------------------------------
wall-clock time of parallel execution
  One of the simplest and most widely used indicators for a parallel program's performance.

## Slide 17: Some General Parallel Terminology
Parallel Overhead
  The amount of time required to coordinate parallel tasks, as opposed to doing useful work. Parallel overhead can include factors such Task start-up time
    Synchronizations
    Data communications
    Software overhead imposed by parallel languages, libraries, operating system, etc.
    Task termination time
Massively Parallel
  Refers to the hardware that comprises a given parallel system - having many processing elements. The meaning of "many" keeps increasing, but currently, the largest parallel computers are comprised of processing elements numbering in the hundreds of thousands
Embarrassingly Parallel
  Solving many similar, but independent tasks simultaneously; little to no need for coordination between the tasks

## Slide 18: Some General Parallel Terminology
Scalability
  Refers to a parallel system's (hardware and/or software) ability to demonstrate a proportionate increase in parallel speedup with the addition of more resources. Factors that contribute to scalability include:
    Hardware - particularly memory-CPU bandwidths and network communication properties
    Application algorithm
    Parallel overhead related
    Characteristics of your specific application

## Slide 19: Why Parallel Computing is necessary?
Rise of multi-core computing machines
Under-utilization of resources
Hyperthreading, introduced by Intel
Notes: This figure shows the single thread performance, CPU clock frequency (MHz), CPU power consumption (watts), and the number of CPU cores from 1970 to 2018. The parallel computing era begins about 2005, when the core count in CPU chips begins to rise, while the clock frequency and power consumption plateaus, yet performance steadily increases.
Hyperthreading: Having two instruction queues interleaving work to the hardware logic units allows a single physical core to appear as two cores to the operating system (OS).

## Slide 20: Example
Let’s take a 16-core CPU with hyperthreading and a 256 bit-wide vector unit, commonly found in home desktops. A serial program using a single core and no vectorization only uses 0.8% of the theoretical processing capability of this processor.
The calculation is
  16 cores × 2 hyperthreads × (256 bit-wide vector unit)/(64-bit double) = 128-way parallelism where 1 serial path/128 parallel paths = .008 or 0.8%. The following figure shows that this is a small fraction of the total CPU processing power.

## Slide 21: Benefits of Parallel Computing
Lesser execution time with multiple cores
Solve larger and complex problems
Energy efficient system
Cost reduction
Notes: Energy efficient: With the emergence of parallel resources in handheld devices, parallelism can speed up applications. This allows the device to return to sleep mode sooner and permits the use of slower, but more parallel processors that consume less power. Thus, moving heavyweight multimedia applications to run on GPUs can have a more dramatic effect on energy efficiency while also resulting in vastly improved performance. The net result of employing parallelism reduces power consumption and extends battery life, which is a strong competitive advantage in this market niche. Another area where energy efficiency is important is with remote sensors, network devices, and operational field-deployed devices, such as remote weather stations. Often, without large power supplies, these devices must be able to function in small packages with few resources. Parallelism expands what can be done on these devices and offloads the work from the central computing system in a growing trend that is called edge compute. Moving the computation to the very edge of the network enables processing at the source of the data, condensing it into a smaller result set that can be more easily sent over the network.

## Slide 22: Process vs threads
An application consists of one or more processes.
Both processes and threads are independent sequences of execution
The typical difference is that threads (of the same process) run in a shared memory space, while processes run in separate memory spaces

## Slide 24: That’s all for today!!