## Slide 1: Parallel & Distributed Computing Lecture 6: Parallel Programming Models
Department of Computer Science
NUML, Islamabad
Farhad M. Riaz
Farhad.Muhammad@numl.edu.pk

## Slide 2: How does parallel computing works?
As a developer, you are responsible for the application software layer, which includes your source code.
In the source code, you make choices about the programming language and parallel software interfaces you use to leverage the underlying hardware.
Additionally, you decide how to break up your work into parallel units.
Approaches a developer can take into
  Process-based parallelization
  Thread-based parallelization
  Vectorization
  Stream (GPU) processing
Notes: Parallelization based on individual processes with their own memory spaces can be distributed memory on different nodes of a computer or within a node. Stream processing is generally associated with GPUs. The model for modern hardware and application software will help you better understand how to plan to port your application to current parallel hardware.

## Slide 3: Example for Sample Application
Perform the computation on a regular two-dimensional (2D) grid of rectangular elements or cells.
The steps prepare for the calculation are
  Discretize (break up) the problem into smaller cells or elements
  Define a computational kernel (operation) to conduct on each element
  Add the following layers of parallelization on CPUs and GPUs to perform the calculation:
    Vectorization
    Threads
    Processes
    Off-loading the calculation to GPUs
Notes: Vectorization—Work on more than one unit of data at a time – Threads —Deploy more than one compute pathway to engage more processing cores – Processes—Separate program instances to spread out the calculation into separate memory spaces – Off-loading the calculation to GPUs—Send the data to the graphics processor to calculate

## Slide 4: Complexity
In general, parallel applications are much more complex than corresponding serial applications.
Not only do you have multiple instruction streams executing at the same time, but you also have data flowing between them.
The costs of complexity are measured in programmer time in virtually every aspect of the software development cycle:
  Design
  Coding
  Debugging
  Tuning
  Maintenance
Adhering to "good" software development practices is essential when working with parallel applications - especially if somebody besides you will have to work with the software.

## Slide 5: Portability
Thanks to standardization in several APIs, such as MPI, POSIX threads, and OpenMP, portability issues with parallel programs are not as serious as in years past.
All of the usual portability issues associated with serial programs apply to parallel programs. For example, if you use vendor "enhancements" to Fortran, C or C++, portability will be a problem.
Even though standards exist for several APIs, implementations will differ in a number of details, sometimes to the point of requiring code modifications in order to effect portability.
Operating systems can play a key role in code portability issues.
Hardware architectures are characteristically highly variable and can affect portability.

## Slide 6: Resource Requirements
The primary intent of parallel programming is to decrease execution wall clock time, however in order to accomplish this, more CPU time is required. For example, a parallel code that runs in 1 hour on 8 processors actually uses 8 hours of CPU time.
The amount of memory required can be greater for parallel codes than serial codes, due to the need to replicate data and for overheads associated with parallel support libraries and subsystems.
For short running parallel programs, there can actually be a decrease in performance compared to a similar serial implementation. The overhead costs associated with setting up the parallel environment, task creation, communications and task termination can comprise a significant portion of the total execution time for short runs.

## Slide 7: Scalability
Two types of scaling based on time to solution: strong scaling and weak scaling.
Strong scaling:
  The total problem size stays fixed as more processors are added.
  Goal is to run the same problem size faster
  Perfect scaling means problem is solved in 1/P time (compared to serial)
Weak scaling:
  The problem size per processor stays fixed as more processors are added. The total problem size is proportional to the number of processors used.
  Goal is to run larger problem in same amount of time
  Perfect scaling means problem Px runs in same time as single processor run

## Slide 8: Parallel Computers
Programming mode types
  Shared Memory
  Distributed Memory
  Hybrid Model

## Slide 9: Parallel Programing Models
Parallel programming models exist as an abstraction above hardware and memory architectures
These models are NOT specific to a particular type of machine or memory architecture
These models can (theoretically) be implemented on any underlying hardware
Examples from past
  SHARED memory model on a DISTRIBUTED memory machine. Kendall Square Research (KSR) ALLCACHE approach, “virtual shared memory"
  DISTRIBUTED memory model on a SHARED memory machine. Message Passing Interface (MPI) on SGI Origin 2000, employed the CC-NUMA type of shared memory architecture, however, MPI commonly done over a network of distributed memory machines
Which model to use?
  Combination of what is available and personal choice

## Slide 10: Shared Memory Architecture
Processors have direct access to global memory and I/O through bus or fast switching network
Cache Coherency Protocol guarantees consistency of memory and I/O accesses
Each processor also has its own memory (cache)
Data structures are shared in global address space
Concurrent access to shared memory must be coordinated
Programming Models
– Multithreading (Thread Libraries)
– OpenMP
P0
Cache
P0
Cache
P1 |  | 
 | Cache | 
Pn
Cache
Global Shared Memory
Shared Bus
...

## Slide 11: Threads Model
Threads implementations commonly comprise:
  A library of subroutines that are called from within parallel source code
  A set of compiler directives imbedded in either serial or parallel source code
Historically, hardware vendors have implemented their own proprietary versions of threads, making it difficult for programmers to develop portable threaded applications
Standardization efforts: POSIX Threads (IEEE POSIX 1003.1c) and OpenMP (Industry standard)
  POSIX Part of Unix/Linux, Library based
  OpenMP Compiler directive based, Portable / multi-platform
  Mircosoft threads, Java, Python threads, CUDA threads for GPUs

## Slide 12: OpenMP
OpenMP: portable shared memory parallelism
Higher-level API for writing portable multithreaded applications
Provides a set of compiler directives and library routines for parallel application programmers
API bindings for Fortran, C, and C++

## Slide 13: Distributed Memory Architecture
Communication Interconne4 ct
P0
...
Each Processor has direct access only to its local memory
Processors are connected via high-speed interconnect
Data structures must be distributed
Data exchange is done via explicit processor-to-processor communication: send/receive messages
Programming Models
  Widely used standard: MPI
  Others: PVM, Express, P4, Chameleon, PARMACS, ...
Memory Memory Memory
P0
P1
Pn

## Slide 14: Message Passing Interface
MPI provides:
Point-to-point communication
Collective operations
  Barrier synchronization
  gather/scatter operations
  Broadcast, reductions
Different communication modes
  Synchronous/asynchronous
  Blocking/non-blocking
  Buffered/unbuffered
Predefined and derived datatypes
Virtual topologies
Parallel I/O (MPI 2)
C/C++ and Fortran bindings

## Slide 15: Hybrid Model
A hybrid model combines more than one of the previously described programming models.
A common example of a hybrid model is the combination of the message passing model (MPI) with the threads model (OpenMP).
Threads perform computationally intensive kernels using local, on-node data
Communications between processes on different nodes occurs over the network using MPI

## Slide 16: Hybrid Model
Another similar and increasingly popular example of a hybrid model is using MPI with CPU-GPU (Graphics Processing Unit) programming.
MPI tasks run on CPUs using local memory and communicating with each other over a network.
Computationally intensive kernels are off-loaded to GPUs onnode.
Data exchange between node-local memory and GPUs uses CUDA (or something equivalent)

## Slide 17: High level programming model
Single Program Multiple Data (SPMD)
Multiple Program Multiple Data (MPMD)

## Slide 18: SPMD
Built upon any combination of the previously mentioned parallel programming models
SINGLE PROGRAM: All tasks execute their copy of the same program simultaneously. This program can be threads, message passing, data parallel or hybrid.
MULTIPLE DATA: All tasks may use different data
-tasks do not necessarily have to execute the entire program
- perhaps only a portion of it

## Slide 19: MPMD
built upon any combination of the previously mentioned parallel programming models
MULTIPLE PROGRAM: Tasks may execute different programs simultaneously.
The programs can be threads, message passing, data parallel or hybrid.
MULTIPLE DATA: All tasks may use different data
MPMD applications are not as common as SPMD applications

## Slide 20: Parallel and Distributed Programming Models
OPENMP
MPI
  For message passing systems
MapReduce and BigTable
  For internet clouds and data centers
Service clouds require extension of Hadoop, EC2, S3 to facilitate distributed computing over distributed storage system
CUDA
  For NVIDIA GPUs
Open Grid Service Architecture (OGSA)
  For grid application development

## Slide 21: Performance, Security and Energy Efficiency
Performance Metrics
  CPU Speed, FLOPS, Job response time, network latency, system throughput, network bandwidth, System overhead (OS boot time, compile time, etc).
Scalability
  Machine (size), software, application, and technology scalability
Amdahl’s law

## Slide 22: Performance, Security and Energy Efficiency
Security
  Threats to system and network
  Confidentiality, integrity, and availability
  Copyright protection
  System Defense technologies
  Data protection infrastructures (IDS)
Energy efficiency
  Distributed power management
  Unused servers’ energy consumption
  Reducing energy in active servers

## Slide 23: That’s all for today!!