## Slide 1: Digital Logic Design Gate-Level Minimization

## Slide 2: 3-1 Introduction
Gate-level minimization refers to the design task of finding an optimal gate-level implementation of Boolean functions describing a digital circuit.

## Slide 3: 3-2 The Map Method
The complexity of the digital logic gates
  The complexity of the algebraic expression
Logic minimization
  Algebraic approaches: lack specific rules
  The Karnaugh map
    A simple straight forward procedure
    A pictorial form of a truth table
    Applicable if the # of variables < 7
A diagram made up of squares
  Each square represents one minterm

## Slide 4: Review of Boolean Function
Boolean function
  Sum of minterms
  Sum of products (or product of sum) in the simplest form
  A minimum number of terms
  A minimum number of literals
  The simplified expression may not be unique

## Slide 5: Two-Variable Map
A two-variable map
  Four minterms
  x' = row 0; x = row 1
  y' = column 0; y = column 1
  A truth table in square diagram
  Fig. 3.2(a): xy = m3
  Fig. 3.2(b): x+y = x'y+xy' +xy = m1+m2+m3
Figure 3.2 Representation of functions in the map
Figure 3.1 Two-variable Map

## Slide 6: A Three-variable Map
A three-variable map
  Eight minterms
  The Gray code sequence
  Any two adjacent squares in the map differ by only on variable
    Primed in one square and unprimed in the other
    e.g., m5 and m7 can be simplified
    m5+ m7 = xy'z + xyz = xz (y'+y) = xz
Figure 3.3 Three-variable Map

## Slide 7: A Three-variable Map
  m0 and m2 (m4 and m6) are adjacent
  m0+ m2 = x'y'z' + x'yz' = x'z' (y'+y) = x'z'
  m4+ m6 = xy'z' + xyz' = xz' (y'+y) = xz'

## Slide 8: Example 3.1
Example 3.1: simplify the Boolean function F(x, y, z) = S(2, 3, 4, 5)
  F(x, y, z) = S(2, 3, 4, 5) = x'y + xy'
Figure 3.4 Map for Example 3.1, F(x, y, z) = Σ(2, 3, 4, 5) = x'y + xy'

## Slide 9: Example 3.2
Example 3.2: simplify F(x, y, z) = S(3, 4, 6, 7)
  F(x, y, z) = S(3, 4, 6, 7) = yz+ xz'
Figure 3.5 Map for Example 3-2; F(x, y, z) = Σ(3, 4, 6, 7) = yz + xz'

## Slide 10: Four adjacent Squares
Consider four adjacent squares
  2, 4, and 8 squares
  m0+m2+m4+m6 = x'y'z'+x'yz'+xy'z'+xyz' = x'z'(y'+y) +xz'(y'+y) = x'z' + xz‘ = z'
  m1+m3+m5+m7 = x'y'z+x'yz+xy'z+xyz =x'z(y'+y) + xz(y'+y) =x'z + xz = z
Figure 3.3 Three-variable Map

## Slide 11: Example 3.3
  Example 3.3: simplify F(x, y, z) = S(0, 2, 4, 5, 6)
  F(x, y, z) = S(0, 2, 4, 5, 6) = z'+ xy'
Figure 3.6 Map for Example 3-3, F(x, y, z) = Σ(0, 2, 4, 5, 6) = z' +xy'

## Slide 12: Example 3.4
Example 3.4: let F = A'C + A'B + AB'C + BC
  Express it in sum of minterms.
  Find the minimal sum of products expression.
  Ans:
  F(A, B, C) = S(1, 2, 3, 5, 7) = C + A'B
Figure 3.7 Map for Example 3.4, A'C + A'B + AB'C + BC = C + A'B

## Slide 13: 3.3 Four-Variable Map
The map
  16 minterms
  Combinations of 2, 4, 8, and 16 adjacent squares
Figure 3.8 Four-variable Map

## Slide 14: Example 3.5
Example 3.5: simplify F(w, x, y, z) = S(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
  F = y'+w'z'+xz'
Figure 3.9 Map for Example 3-5; F(w, x, y, z) = Σ(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14) = y' + w' z' +xz'

## Slide 15: Example 3.6
Example 3-6: simplify F = ABC + BCD + ABCD + ABC
Figure 3.9 Map for Example 3-6; ABC + BCD + ABCD + ABC= BD + BC +ACD

## Slide 16: Prime Implicants
Prime Implicants
  All the minterms are covered.
  Minimize the number of terms.
  A prime implicant: a product term obtained by combining the maximum possible number of adjacent squares (combining all possible maximum numbers of squares).
  Essential P.I.: a minterm is covered by only one prime implicant.
  The essential P.I. must be included.

## Slide 17: Prime Implicants
Consider F(A, B, C, D) = Σ(0, 2, 3, 5, 7, 8, 9, 10, 11, 13, 15)
  The simplified expression may not be unique
  F = BD+B'D'+CD+AD = BD+B'D'+CD+AB'
  = BD+B'D'+B'C+AD = BD+B'D'+B'C+AB'
Figure 3.11 Simplification Using Prime Implicants

## Slide 18: 3.4 Five-Variable Map
Map for more than four variables becomes complicated
  Five-variable map: two four-variable map (one on the top of the other).
Figure 3.12 Five-variable Map

## Slide 19
Table 3.1 shows the relationship between the number of adjacent squares and the number of literals in the term.

## Slide 20: Example 3.7
Example 3.7: simplify F = S(0, 2, 4, 6, 9, 13, 21, 23, 25, 29, 31)
F = A'B'E'+BD'E+ACE

## Slide 21: Example 3.7 (cont.)
Another Map for Example 3-7
Figure 3.13 Map for Example 3.7, F = A'B'E'+BD'E+ACE

## Slide 22: 3-5 Product of Sums Simplification
Approach #1
  Simplified F' in the form of sum of products
  Apply DeMorgan's theorem F = (F')'
  F': sum of products → F: product of sums
Approach #2: duality
  Combinations of maxterms (it was minterms)
  M0M1 = (A+B+C+D)(A+B+C+D') = (A+B+C)+(DD') = A+B+C
M0 | M1 | M3 | M2
M4 | M5 | M7 | M6
M12 | M13 | M15 | M14
M8 | M9 | M11 | M10
00
01
11
10
00
01
11
10
AB
CD

## Slide 23: Example 3.8
  Example 3.8: simplify F = S(0, 1, 2, 5, 8, 9, 10) into (a) sum-of-products form, and (b) product-of-sums form:
Figure 3.14 Map for Example 3.8, F(A, B, C, D)= S(0, 1, 2, 5, 8, 9, 10) = B'D'+B'C'+A'C'D
  F(A, B, C, D)= S(0, 1, 2, 5, 8, 9, 10) = B'D'+B'C'+A'C'D
  F' = AB+CD+BD'
    Apply DeMorgan's theorem; F=(A'+B')(C'+D')(B'+D)
    Or think in terms of maxterms

## Slide 24: Example 3.8 (cont.)
Gate implementation of the function of Example 3.8
Figure 3.15 Gate Implementation of the Function of Example 3.8
Product-of sums form
Sum-of products form

## Slide 25: Sum-of-Minterm Procedure
Consider the function defined in Table 3.2.
  In sum-of-minterm:
  In sum-of-maxterm:
  Taking the complement of F

## Slide 26: Sum-of-Minterm Procedure
Consider the function defined in Table 3.2.
  Combine the 1’s:
  Combine the 0’s :
Figure 3.16 Map for the function of Table 3.2
'

## Slide 27: 3-6 Don't-Care Conditions
The value of a function is not specified for certain combinations of variables
  BCD; 1010-1111: don't care
The don't-care conditions can be utilized in logic minimization
  Can be implemented as 0 or 1
Example 3.9: simplify F(w, x, y, z) = S(1, 3, 7, 11, 15) which has the don't-care conditions d(w, x, y, z) = S(0, 2, 5).

## Slide 28: Example 3.9 (cont.)
  F = yz + w'x'; F = yz + w'z
  F = S(0, 1, 2, 3, 7, 11, 15) ; F = S(1, 3, 5, 7, 11, 15)
  Either expression is acceptable
Figure 3.17 Example with don't-care Conditions

## Slide 29: 3-7 NAND and NOR Implementation
NAND gate is a universal gate
  Can implement any digital system
Figure 3.18 Logic Operations with NAND Gates

## Slide 30: NAND Gate
Two graphic symbols for a NAND gate
Figure 3.19 Two Graphic Symbols for NAND Gate

## Slide 31: Two-level Implementation
Two-level logic
  NAND-NAND = sum of products
  Example: F = AB+CD
  F = ((AB)' (CD)' )' =AB+CD
Figure 3.20 Three ways to implement F = AB + CD

## Slide 32: Example 3.10
Example 3-10: implement F(x, y, z) =
Figure 3.21 Solution to Example 3-10

## Slide 33: Procedure with Two Levels NAND
The procedure
  Simplified in the form of sum of products;
  A NAND gate for each product term; the inputs to each NAND gate are the literals of the term (the first level);
  A single NAND gate for the second sum term (the second level);
  A term with a single literal requires an inverter in the first level.

## Slide 34: Multilevel NAND Circuits
Boolean function implementation
  AND-OR logic → NAND-NAND logic
    AND → AND + inverter
    OR: inverter + OR = NAND
    For every bubble that is not compensated by another small circle along the same line, insert an inverter.
Figure 3.22 Implementing F = A(CD + B) + BC

## Slide 35: NAND Implementation
Figure 3.23 Implementing F = (AB +AB)(C+ D)

## Slide 36: NOR Implementation
NOR function is the dual of NAND function.
The NOR gate is also universal.
Figure 3.24 Logic Operation with NOR Gates

## Slide 37: Two Graphic Symbols for a NOR Gate
Example: F = (A + B)(C + D)E
Figure 3.26 Implementing F = (A + B)(C + D)E
Figure 3.25 Two Graphic Symbols for NOR Gate

## Slide 38: Example
Example: F = (AB +AB)(C + D)
Figure 3.27 Implementing F = (AB +AB)(C + D) with NOR gates

## Slide 39: 3-8 Other Two-level Implementations (
Wired logic
  A wire connection between the outputs of two gates
  Open-collector TTL NAND gates: wired-AND logic
  The NOR output of ECL gates: wired-OR logic
AND-OR-INVERT function
OR-AND-INVERT function
Figure 3.28 Wired Logic

## Slide 40: Non-degenerate Forms
16 possible combinations of two-level forms
  Eight of them: degenerate forms = a single operation
    AND-AND, AND-NAND, OR-OR, OR-NOR, NAND-OR, NAND-NOR, NOR-AND, NOR-NAND.
  The eight non-degenerate forms
    AND-OR, OR-AND, NAND-NAND, NOR-NOR, NOR-OR, NAND-AND, OR-NAND, AND-NOR.
    AND-OR and NAND-NAND = sum of products.
    OR-AND and NOR-NOR = product of sums.
    NOR-OR, NAND-AND, OR-NAND, AND-NOR = ?

## Slide 41: AND-OR-Invert Implementation
AND-OR-INVERT (AOI) Implementation
  NAND-AND = AND-NOR = AOI
  F = (AB+CD+E)'
  F' = AB+CD+E (sum of products)
Figure 3.29 AND-OR-INVERT circuits, F = (AB +CD +E)

## Slide 42: OR-AND-Invert Implementation
OR-AND-INVERT (OAI) Implementation
  OR-NAND = NOR-OR = OAI
  F = ((A+B)(C+D)E)'
  F' = (A+B)(C+D)E (product of sums)
  Figure 3.30 OR-AND-INVERT circuits, F = ((A+B)(C+D)E)'

## Slide 43: Tabular Summary and Examples
Example 3-11: F = x'y'z'+xyz'
  F' = x'y+xy'+z (F': sum of products)
  F = (x'y+xy'+z)' (F: AOI implementation)
  F = x'y'z' + xyz' (F: sum of products)
  F' = (x+y+z)(x'+y'+z) (F': product of sums)
  F = ((x+y+z)(x'+y'+z))' (F: OAI)

## Slide 44: Tabular Summary and Examples

## Slide 45
  Figure 3.31 Other Two-level Implementations

## Slide 46: 3-9 Exclusive-OR Function
Exclusive-OR (XOR)
  xÅy = xy'+x'y
Exclusive-NOR (XNOR)
  (xÅy)' = xy + x'y'
Some identities
  xÅ0 = x
  xÅ1 = x'
  xÅx = 0
  xÅx' = 1
  xÅy' = (xÅy)'
  x'Åy = (xÅy)'
Commutative and associative
  AÅB = BÅA
  (AÅB) ÅC = AÅ (BÅC) = AÅBÅC

## Slide 47: Exclusive-OR Implementations
Implementations
  (x'+y')x + (x'+y')y = xy'+x'y = xÅy
Figure 3.32 Exclusive-OR Implementations

## Slide 48: Odd Function
  AÅBÅC = (AB'+A'B)C' +(AB+A'B')C = AB'C'+A'BC'+ABC+A'B'C = S(1, 2, 4, 7)
  XOR is a odd function → an odd number of 1's, then F = 1.
  XNOR is a even function → an even number of 1's, then F = 1.
Figure 3.33 Map for a Three-variable Exclusive-OR Function

## Slide 49: XOR and XNOR
Logic diagram of odd and even functions
Figure 3.34 Logic Diagram of Odd and Even Functions

## Slide 50: Four-variable Exclusive-OR function
Four-variable Exclusive-OR function
  AÅBÅCÅD = (AB'+A'B)Å(CD'+C'D) = (AB'+A'B)(CD+C'D')+(AB+A'B')(CD'+C'D)
Figure 3.35 Map for a Four-variable Exclusive-OR Function

## Slide 51: Parity Generation and Checking
Parity Generation and Checking
  A parity bit: P = xÅyÅz
  Parity check: C = xÅyÅzÅP
    C=1: one bit error or an odd number of data bit error
    C=0: correct or an even # of data bit error
Figure 3.36 Logic Diagram of a Parity Generator and Checker

## Slide 52: Parity Generation and Checking

## Slide 53: Parity Generation and Checking

## Slide 54: 3.10 Hardware Description Language (HDL)
Describe the design of digital systems in a textual form
  Hardware structure
  Function/behavior
  Timing
VHDL and Verilog HDL

## Slide 55: A Top-Down Design Flow
Specification
RTL design and
Simulation
Logic Synthesis
Gate Level Simulation
ASIC Layout
FPGA Implementation

## Slide 56: Module Declaration
Examples of keywords:
module, end-module, input, output, wire, and, or, and not
Figure 3.37 Circuit to demonstrate an HDL

## Slide 57: HDL Example 3.1
HDL description for circuit shown in Fig. 3.37

## Slide 58: Gate Displays
Example: timescale directive
  ‘timescale 1 ns/100ps

## Slide 59: HDL Example 3.2
Gate-level description with propagation delays for circuit shown in Fig. 3.37

## Slide 60: HDL Example 3.3
Test bench for simulating the circuit with delay

## Slide 61: Simulation output for HDL Example 3.3

## Slide 62: Boolean Expression
Boolean expression for the circuit of Fig. 3.37
Boolean expression:
HDL Example 3.4

## Slide 63: HDL Example 3.4

## Slide 64: User-Defined Primitives
General rules:
Declaration:
Implementing the hardware in Fig. 3.39

## Slide 65: HDL Example 3.5

## Slide 66: HDL Example 3.5 Continued)

## Slide 67
Figure 3.39 Schematic for circuit with_UDP_02467